## Slide 1: Spectrum Scale : Tier 0 Pattern - High Level Target Design
IDEA Justification for vMotion support for Scale RDM nodes.
8th AUG 2022
0.11

## Slide 2
Spectrum Scale Design REVIEW
Scale Requirements / Recommendations | Description | Open Clarifications
IBM Spectrum Scale support statement | Spectrum Scale support statement with VMware. For RDM Direct Attach or VMDK - vMotion (DRS) is not supported, and FT is not supported. Impacted Scale components: NSD Scale nodes, and Quorum nodes. Does not impact Scale client. | 
What is Supported? | GPFS nodes with no direct disk access = Spectrum Scale CLIENT. vSphere vMotion is supported vSphere Fault Tolerance (FT) is not supported Local read-only cache is not supported | 
IBM Spectrum Scale support statement explanation | VMware vMotion is not a supported combination with Scale NSD as these are two different cluster managers working independently. Justification (1): Spectrum Scale is heavily dependent on network traffic, if you use vMotion or FT, you will disconnect the networking from the virtual machines for the time it takes for the machines to move between hosts (default timeout for a vMotion is 100 seconds). This will cause Scale nodes in the cluster to expel the node(s) that are being migrated by vMotion, due to network timeouts – the Scale timeout is 30 seconds. A multi-event vMotion (multiple concurrent vMotions affecting RDM Direct attached VMs) will result in massive instability in the Scale cluster. Which will lead to a Scale cluster panic - locking up the entire cluster, or taking all the nodes offline and crashing the entire cluster. Further DEV clarification 01/08/2022: With DRS enabled (automatic or manual), Scale DEV are concerned about lose of communication and the length of lose of communication for Scale nodes with direct access (RDM)s during a vMotion event. Justification (2): a loss of data in cache during a vMotion event, event unlikely but not impossible. If a loss of data in cache were to occur, Scale behaviour: Direct memory not de-staged, data out of sync, could lead to inconsistent data, causing I/O errors. Remediation would be required on filesystem check to restore the integrity of the fs check. | 

## Slide 3
Spectrum Scale Design REVIEW
Scale Requirements / Recommendations | Description | Open Clarifications
HSBC Standards: Virtualization / VMware | DRS Enabled for all ESXi hosts / VMs. Policy default is Automatic. Optionally can be set to Manual. CANNOT be disabled. Design requires that anti-affinity set to true. Never have more than 1 VM (for any part of the SFG/Scale design) on each ESXi node within a single cluster– no colocation of VMs associated with this service within a single ESXi node within 1 cluster. Confirm VMware DRS policy / constraints on public cloud (3rd DC Quorum sites) For Manual DRS - Can sequencing of app start be pre-defined? | 
 | HSBC experience of DRS normal behaviour duration is “unnoticeable” – less than 30 seconds. Understand measured, expected, design point for DRS vMotion event duration. Document scenarios where a vMotion event for one host may take longer than 30secs | 
 | Any design cannot prevent 24/7 patching. To confirm is the requirement 24/7 AUTOMATED patching? | 
HSBC OPEN Clarifications | DRS ENABLED (Automated): this is not a negotiation around the configuration & offering of the shared virtualisation infrastructure within HSBC. Your technology & services either supports vMotion or it doesn’t. | 
IBM Spectrum Scale requested information | DEV have requested further details on the proposed HSBC design specification. This is provide further context for DEV to EXPLAIN the rational behind the no DRS support statement. Do we know any of the following information for HSBC’s config: VM OS VM Version for Spectrum Scale nodes (NSD and Quorum) VMware version (all components) Storage connectivity: rdm vs vmdk, multi-writer vs single-writer Network connectivity between ESX machines: is vMotion on a different network than mgmt. and a different network than Spectrum Scale? What is the DRS ruleset? What typically triggers a vmotion and is it for both storage and compute or one of these? What is the SLA for a vMotion to complete in and under what circumstances doesn’t that not occur and how often? | 
Related HSBC Design Decisions: | RDM required part of the design for SS, as need LUNs to be available between two of more servers. A mandatory part of the resilient architecture of SS design is based on twin tailed LUNs between two NSD Scale nodes. VMware – min 16 ESXi nodes per cluster, per DC. Cluster does not spread across DCs. DRS policy placement is bound within a single cluster. VMware DR design – if a full cluster failure occurs – what HA or DR event takes place, by what components? | 
Spectrum Scale RDM no support with DRS and FT

## Slide 4
Spectrum Scale Design REVIEW
Scale Requirements / Recommendations | Description | Open Clarifications
HSBC SFG Design INTEGRATION | Design considerations: 4 x SFG nodes, split across 2 x DCs. Connected by GLSB. Per site - SFG nodes sized for 200% of prod traffic (N+1 capacity sizing) Confirm any SFG consideration with DRS. | 
HSBC Topology Mitigation Options |  | 
HSBC Required timeline for design finalisation | PENDING confirmation of US / Wholesale milestone dates. – Q3- Q4 2022 previous target. | 
Proposed HSBC Scale Design | PENDING response to actions. | 
HSBC Agreed Scale Design: | PENDING | 
Spectrum Scale RDM no support with DRS and FT
Mitigation Options | IBM Spectrum Scale Support status | HSBC Viability
DRS set to MANUAL on collocated SFG/SS VMs. | No Support remains only formal support position at this time. IBM DEV – standard request for functional enhance has been raised, and will be assessed for viability and duration. Add other (warmer) DEV statement here. | 
Split out SFG and SS into separate VMs. DRS set to AUTOMATIC on SFG VMs. DRS set to MANUAL on SS VMs – NSD Scale nodes and Quorum nodes. | For Scale RDM: No Support remains only formal support position at this time. IBM DEV – standard request for functional enhance has been raised, and will be assessed for viability and duration. Add other (warmer) DEV statement here. | 
DRS set to MANUAL LINK | No Support remains only formal support position at this time | Project UAT testing plan Project risk defined accepted and signed off.
Separate PHYSICAL clusters for SCALE storage cluster. Likely to require separate physical servers. | By-passes DRS support statement. | Non-standard Viability assessment possibly not positive on this as an option to consider.

## Slide 5
Spectrum Scale CLIENT REQUEST CONTEXT
CAT | Description
Client Context | HSBC – globally have selected IBM Spectrum Scale as the geographically dispersed file systems to improve the resilience and failure tolerance of Sterling Business Integrator (SBI) + Sterling File Gateway (SFG). Pilot complete, moving into detailed design for UAT built in Q3 2022.
SFG Overview | Real time payments processing, all SBI require simultaneous r / w access to all SWIFT RA files written by other nodes. Providing PAYMENTS services based on IBM Sterling Business Integration, is a high value, highly critical revenue generating service for the Payments traffic. Payments are highly time sensitive, high in revenue value and availability of the service is critical. For multi Availability Zone high availability, with no data loss, Sterling Integrator's architecture depends on a matching multi Availability Zone high-availability filesystem The filesystem chosen must be in a multi Availability Zone, highly available, RPO=0, RTO=0 designed filesystem, in order to match the project's RPO=0 and RTO=0. The architecture of Sterling Integrator means that the data at all sites must be writable, and in sync at all times. SWIFT messaging / payload are transient – stored for max 3 days. Files are small is size – <1MB per file. Volume is high – HSBC US geo – 280k messages per day (busiest cluster). Amazon is one of their primary customers – payments processing. Tik Tok in addition.
HSBC Sizing | Tier 1 service. Continuous availability requirement, zero downtime. Will have multiple Scale clusters in each geo – UK, US, HK, Mexico.
HSBC OS | Versions • vCenter 7.0.3d • VMware ESXi 6.7.0 build-18828794 (currently upgrading to v7.0.3d) • VM Version would be no higher than v15 to support 6.7 at the moment. • ESXi Storage is typically SAN or iSCSI based o SAN PURE and VMAX3 o iSCSI PURE Only • Volumes are vmdk • RDMs only on SAN FC Storage not iSCSI. o iSCSI recently has a option for multi-writer under test but only for one use case but could be considered as needed. o RDMs we limit to 2-4 per VM max depending on the use case at the moment to stop people requesting too many and maxing out our clusters Max LUN counts.

## Slide 6: IBM sign-off
The information contained in this email is being provided by IBM as a matter of courtesy and provided "AS-IS" without any direct and implied warranty; IBM assumes no liability. “Please note that the solution and price information provided is indicative and is intended to be for general guidance only. It is based on the limited requirements information we have received, our experience of performing projects and services of a similar type, scale and complexity for other customers, and the key assumptions listed.